## Slide 1: Modelling for control of autonomous marine vehicles
Autonomous Marine Robotics – Training session 2

## Slide 2: Exercise 1 – Vehicle kinematics
An autonomous marine vehicle is sailing with a constant speed U = 10 knots and a constant heading φ = -25 degrees. Assuming that the motion of the craft is restrained to the horizontal plane and no ocean current is present, compute the following:
  Derive the continuous time kinematic model that describes the motion of the autonomous marine vehicle in the tangential frame
  Implement the obtained model in Matlab/Simulink
  Determine the position of the craft in the tangential frame at time t = 250s given the initial conditions N0 = 1000m; E0 = -35m; φ0 = -25deg.
  Plot the trajectory of the marine craft in the tangential frame

## Slide 3: Exercise 1 – Vehicle kinematics
Assume that a constant current is now present in the geographical area where the marine craft is operating. The current velocity is Vc = 1.5 m/s and its direction is βc = 65 degrees. Compute the following:
  Modify the continuous time kinematic model to include the action of the ocean current
  Adapt the Matlab/Simulink model to include the action of an ocean current
  Repeat 1.C
  Repeat 1.D

## Slide 4: Exercise 1 – Vehicle kinematics
A remotely operated vehicle is descending the water column by following a helix of radius a = 5m and a pitch 2πb, where b = 0.25m/s (Info about helix @ https://en.wikipedia.org/wiki/Helix). Assuming that the descend time is 240 seconds, compute the following
  Derive the continuous time kinematic model describing the motion of the marine craft in the tangential frame
  Implement the obtained model in Matlab/Simulink
  Determine the position of the ROV at time t = 120s and at end of the descend, given the initial conditions N0 = 0m; E0 = 100m; D0 = 10m; φ0 = 90deg.
  Plot the trajectory of the ROV in the tangential frame

## Slide 5: Exercise 2 – Vehicle kinetics