## Slide 1: Path Planning
Autonomous Marine Robotics – Training session 3

## Slide 2: Exercise 1 – Searching Based Path Planning
Run the Python Jupyter Notebook (exe1_search_based.ipynb)
  The project is available from the Gitlab repository under directories: Training Sessions\TS3 Path Planning Notebook
Discuss the comparison among BFS, Dijkstra, A* with Euclidean Heuristics and A* with Manhattan Heuristics.

## Slide 3: Exercise 2 – Sampling Based Path Planning
Exercise 2.1
  Run the Python Jupyter Notebook (exe2_sampling_based.ipynb)
  Complete the code for tuning other hyperparameters of RRT*:
    Goal sample rate
    Searching radius
Exercise 2.2
  Run the Python Jupyter Notebook (exe2_sampling_based_seachart.ipynb)
  Complete the code, implementing RRT*
  Compare the result between RRT and RRT*.

## Slide 4: Exercise 3 – Implementation using BlueROV Simulator
Exercise 3.1: Running the path planning simulation
  The ROS workspace is at “Training_Sessions/TS3_Path_Planning/ts3_ws”
  You need to compile it by:
    cd 34763-autonomous-marine-robotics\Training_Sessions\TS3_Path_Planning\ts3_ws
    catkin_make
  How to run the simulation:
    Run the BlueROV Gazebo:
      source devel/setup.bash
      roslaunch ts3_path_planning start_pid_demo_lake.launch
    Run the map publisher, path planner and path follower:
      source devel/setup.bash
      roslaunch ts3_path_planning run.launch
    Publish the goal position:
      source devel/setup.bash
      roslaunch ts3_path_planning publish_goal.launch

## Slide 5: Exercise 3 – Implementation using BlueROV Simulator
Exercise 3.2: Add a new A* path planner ROS node:
  Duplicate dijkstra_planner.py
  Add heuristic function (See the code from the Exercise 1)
    PathPlanning\Search_based_Planning\Search_2D\Astar.py
  Add a new or modify the ROS launch file to call your new ROS node: run.launch
  Update the CMakeLists.txt (adding your new python file) and compile (catkin_make)

## Slide 6: Exercise 4 – 3D Path Planning
Exercise 4.1
  Duplicate and extend exe2_1_sampling_based.ipynb to 3D. The classes are available in: PathPlanning/Sampling_based_Planning/Search_3D
Exercise 4.2
  Implement one of the 3D path planning algorithm to the BlueROV simulator
  Hints:
    The gridmap is available in Exercise-3 (The topic name is “grid_map” which can be converted to “pointcloud”). See: grid_map_ros/src/GridMapRosConverter.cpp
    The pointcloud can be converted to octomap (3D occupancy grid map): octomap - ROS Wiki
    There is a repository for octomap collision check: 3d_navigation/octomap_collision_check at hydro-devel · ros-planning/3d_navigation (github.com)
    You are also welcome to use octomap python library: wkentaro/octomap-python: Python binding of the OctoMap library. (github.com) or other techniques