## Slide 1: Introduction to BlueROV and Simulator
34763 Autonomous Marine Robotics Course (Training)

## Slide 2: Outlines
Training Activities
About BlueROV
  Hardware
  Software
BlueROV simulators
  UUV simulator (ROS+Gazebo)
  Software In The Loop with Pixhawk PX4
  Ground control station - Mission planning
This week activities
  Setting up simulator (using Docker)
  BlueROV teleoperation simulation using ROS

## Slide 3: Training Activities
Getting started with simulators
Identification of linear models
Path planning 2D and 3D
Controllers tuning (PID)
Pose estimation tuning (EKF)
Neptus for mission planning
Group assignments
Deployment using real robots

## Slide 4: About BlueROV
BlueROV1
BlueROV2
BlueROV2 - Heavy

## Slide 5: BlueROV Hardware
BlueROV1 (2016)

## Slide 6: BlueROV Hardware
BlueROV2-R3

## Slide 7: BlueROV Hardware
BlueROV2-R4 (Newest Version)

## Slide 8: Sensors
Sonar:
  Ping 1D
  Side Scan Sonar
  Multibeam Imaging Sonar
  Water Linked DVL
IMU (Built-in Pixhawk PX4 and Navigator Controller)
Leak (Built-in Navigator Controller)
Depth/Pressure Sensor
Temperature Sensor
Low-light Camera
External Navigation Aids
HiPAP - Acoustic underwater positioning and navigation systems - Kongsberg Maritime

## Slide 9: BlueROV Software
BlueROV1 until BlueROV2-R3
BlueROV2-R4

## Slide 10: BlueROV Simulators
Gazebo + ROS (UUV Simulator)
  Environmental effects: Ocean waves, buoyancy
  Sensors:
    Camera
    Chemical concentration
    Sonar
    DVL
  Low-level control: PID, MPC
  Advanced practice: Pose estimation (EKF), SLAM
  Programming languages: Python, C++
Furthermore: uuvsimulator.github.io

## Slide 11: BlueROV Simulators
Software In The Loop Simulation (SITL)
  Simple (Ardupilot Sim + QGroundcontrol)
  Advanced (Gazebo + ROS + Ardupilot Sim + QGroundcontrol)
Ardupilot Simulator Map and Console
QGroundcontrol

## Slide 12: Activities
Getting started with simulators
  Docker installation
  Build and run docker file
BlueROV2 manual control
Visit: bit.ly/AMR34763
For today activity, please use the docker file inside noetic-minimum folder

## Slide 13: Activities
Open Gazebo and spawn the robot:
  roslaunch bluerov2_gazebo start_pid_demo.launch

## Slide 14: Activities
Inspect all ROS topics:
  rostopic list
  rostopic echo <topic_name>
  rosrun rqt_graph rqt_graph

## Slide 15: Activities
Make the robot moves by using keyboard:
  roslaunch uuv_teleop uuv_keyboard_teleop.launch uuv_name:=bluerov2

## Slide 16: Activities
Make the robot moves using RQT publisher:
  rosrun rqt_publisher rqt_publisher
  Add /bluerov2/cmd_vel, change the value of linear-x to 0.5 to 1, check the checkbox to publish
  You can change the rate to make the move faster
  You can do experiment by changing another variable (linear y, z or angular z)

## Slide 17: Activities
Make the robot moves using python script!
  Using python script as a ROS node to publish bluerov2/cmd_vel value
    How to run:
      rosrun bluerov_simple_command square_wave_surge_command.py
    Now, your robot should move.
    You can open the project using Visual Studio Code
      File –> Open Folder
      Open this folder: /home/ubuntu/course_ws/src
    The script is at
      /home/ubuntu/course_ws/src/bluerov_simple_command/src/square_wave_surge_command.py

## Slide 18: Activities
Make the robot moves to another direction!
  Next, create a new python file named square_wave_heading_command.py by copying the existing file (square_wave_surge_command.py)
  Change the ROS node name at line 8
  Modify the file so that it publishes positive twist_msg.angular.z instead of twist_msg.linear.x
  Modify the CMakeLists.txt by adding square_wave_heading_command.py
  Compile the project:
    cd /home/ubuntu/course_ws
    catkin_make
    source devel/setup.bash
  Run the new file:
    rosrun bluerov_simple_command square_wave_heading_command.py

## Slide 19: Activities
Plot the values!
  rosrun rqt_plot rqt_plot

## Slide 20: Activities
Further reading:
  Official ROS Wiki:
    Documentation - ROS Wiki
  ROS tutorial:
    Programming for Robotics - ROS – Robotic Systems Lab | ETH Zurich