## Slide 1: Introduction to BlueROV and Simulators
Special Course: Autonomous Marine Robotics

## Slide 2: Topics
Introduction
BlueROV (v1 & v2) system overview
Simulators
  ArduSub SITL
  Unmanned Underwater Vehicle Simulator
  Marine Systems Simulator Toolbox (MATLAB)
Activities (ArduSub SITL)
  Simulating BlueROV2
  Changing BlueROV2 Control State
  Understanding the MAVROS interface

## Slide 3: ROV – Remotely Operated Vehicle
Tethered to Control Station
  Low Latency Feedback
Vectored Thrusting
  Fully/Over-actuated Control
Hydrostatically Stable, but low hydrodynamic efficiency.
  Low speeds (< 2 knots)
1 knot ≈ 0.5144 m/s
https://oceanexplorer.noaa.gov/technology/subs/hercules/hercules.html
https://www.youtube.com/watch?v=woTi--GCzwM&ab_channel=EVNautilus
Nautilus Live: Biologists Live Stream the Benthic
Mission to Europa
https://robotik.dfki-bremen.de/en/research/projects/eurex.html
Notes: Question: This is a german submarine @ 1500 m depth. How did they get this picture?
QUESTION: Knots to m/s, does anybody know?

## Slide 4: BlueROV
50/50 Open-Source Development, Engineered Sensors & Electronics
Three variants
  R1 (1-5 models @ Elektro)
  R2 (1-2 models @ Aqua)
  R2-Heavy
Frame Configurations

## Slide 5: BlueROV

## Slide 6: BlueROV Accompanied Flight Controller System
4 Levels of Structure
  Sensor Readings & Open Loop Control (Lowest Level)
  Hardware State Management & Closed Loop Control (PID)
  Advanced Onboard Devices, Proxy Server Interfacing, Highest levels of Onboard Control
  Human Machine Interface, Shoreside Processing, External Navigation Aids
F LIGHT
C ONTROLLER
U NIT
C OMPANION
C OMPUTER
G ROUND
C ONTROL
S TATION

## Slide 7: Flight Controller Unit
Microcontroller combined with IMU
Flashed with ArduSub control software
Controls thrusters
  Manual Open Loop (Joystick)
  Stabilized (Pitch & Roll Closed Loop)
  Depth (Stabilized + Depth Closed Loop)

## Slide 8: Companion Computer
Embedded System (Raspberry Pi)
Middle-man between FCU and GCS
Extra Sensors (Camera, Altimeter)
Additional Software Packages

## Slide 9: Ground Control (Topside) Station
Human Machine Interface
Joystick
External Navigation Aids
  Acoustic Base Line Systems
  GPS (Ship or Stationary)
Additional Software Packages
  Logging, Video Streaming

## Slide 10: External Navigation Aid
Acoustic Baseline System (“Underwater GPS”)
Long Baseline (LBL)
Short Baseline (SBL)
Ultra-short Baseline (USBL)

## Slide 11: Further Reading on BlueROV
In-depth Presentation on BlueROV (Best to Mute): https://slideplayer.com/slide/10977661/
Waterlinked Short Baseline: https://waterlinked.com/underwater-gps/
Blue Robotics Forums: https://discuss.bluerobotics.com/
ArduSub source code: https://github.com/ArduPilot/ardupilot/tree/master/ArduSub
Questions?

## Slide 12: Simulating the BlueROV2
Physics Environment
Interface
MAVROS

## Slide 13: Which Simulator is Better?
No Perfect Fit
ArduPilot (ArduSub SITL) | Gazebo (UUV Simulator)
Lightweight (CPU Friendly) | CPU Heavy
Plug & Play (Interchange HW / SW) | No FCU readily available
Modelled to BlueROV2 | Can simulate any vehicle
No Camera | Can simulate cameras, DVL sonar etc.
Simple collision (seabed) | Collision with models
Suggested BlueROV2 “Pain Free“™ Workflow
Design “Amazing System” in ROS with ArduSub backend
Do extensive testing in SITL
Implement on Real Vehicle!

## Slide 14: Simulating the BlueROV2
Installation Checklist
Found Open-Source Simulator Software Web Page in DTU Learn
  https://github.com/DTUAqua-ObsTek/bluerov2
Installed Ubuntu 20.04 (or virtual machine)
Installed ROS Noetic Ninjemys Desktop
  MAVROS
Installed ArduPilot and compiled ArduSub SITL
Installed QGroundControl

## Slide 15: Activities!
Make sure to cd into your clone/fork of the bluerov2 repository.
Run the following to pull in the latest changes:
git pull origin master
Navigate to: The BlueROV2 ROS Stack