## Slide 1: Experiment with the Real BlueROV
34763 Autonomous Marine Robotics Course (Training)

## Slide 2: Available Robots
BlueROV1 (Galatea)
  Tested: ROS (kinetic), Pixhawk PX4, connection with QGroundcontrol via ethernet, Ping 1D sensor, all thrusters work
  Needs: Battery, Laptop for GCS
BlueROV1 (Sycillia)
  Tested: Not yet
  Needs: Battery, Laptop for GCS
BlueROV2?

## Slide 3: Getting Started BlueROV1
BlueROV1 (Galatea)
  Access SSH via ethernet:
    Open Windows command prompt or Linux/MAC terminal.
    ssh odroid@10.0.0.22 (password: odroid)
  Open your PC/laptop, open Windows command prompt or Linux/MAC terminal.
    For windows: ipconfig
    For Linux/MAC: ifconfig
    Note your PC/laptop’s IP address
  Back to the 1st terminal: roslaunch bluerov bluerov_r1.launch gcs_url:=“udp://@<ip address>:14550” fcu_url:=“/dev/ttyACM0:115200”
  Make sure you have installed Qgroundcontrol: Downloads - QGroundControl - Drone Control and open it.
  The vehicle should appear in Qgroundcontrol now.

## Slide 4: Access the Ping1D sensor
BlueROV1 (Galatea)
  Make sure the ping sensor is connected to the Odroid via USB to serial uart. You can check it by doing “ls /dev” and see that ttyUSB0 exists.
  Start the ping1d node:
    roslaunch ping1d ping1d.launch
  You should be able to get the “sonar_data” value:
    rostopic echo sonar_data

## Slide 5: Getting Started with QGroundcontrol
Once the robot is connected to the Qgroundcontrol, you can check the:
  Sensors:
  Thrusters: